## Slide 1: Intel 8085
Unit 2

## Slide 2
8085 is an 8-bit microprocessor as it operates on 8 bits at a time. This microprocessor exhibits some unique characteristics and this is the reason it still holds popularity among the microprocessors.
Basically, 8085 was the first commercially successful microprocessor by Intel. As some of the architectural drawbacks associated with 8080 was also eliminated by 8085.
The size of the data bus of 8085 is 8 bits while that of the address bus is 16. Therefore, can address 64 KB (i.e., 216) memory. Also, as it can perform 8-bit operation thus the size of ALU is also 8-bit.

## Slide 3
It can perform different operations :
Operates on and stores 8-bit data.
It executes arithmetic and logic operations.
8085 also sequences the instructions to be executed.
Stores data temporarily.
In order to perform all such operations, the processor needs a control unit, arithmetic logic unit, registers, buses etc.

## Slide 4: Block diagram of 8085

## Slide 5
8085 Microprocessor :: Instruction and Data Flow
An instruction is a binary pattern designed to perform a specific function. The list of entire instructions is called the instruction set. The instruction set determines what function the microprocessor can perform.
The following notations are used in the description of the instructions:
R = 8085 8-bit registers (B, C, D, E, H, L)
M = memory register (location) pointed by value HL
Rs = register source
Rd = register destination (B, C, D, E, H, L)
Rp = register pair (BC, DE, HL)
( ) = contents of

## Slide 6
1. Data Transfer (copy) Instructions
These instructions perform the following six operations:
  Load 8-bit number in a register.
  Load 16-bit number in a register pair.
  Copy from register to register.
  Copy between register and memory.
  Copy between I/O and accumulator.
  Copy between registers and stack memory.
  MVI R, 8-bit
  MOV Rd, Rs
  LXI Rp, 16-bit
  OUT 8-bit
  IN 8-bit
  LDA 16-bit
  STA 16-bit
  LDAX Rp
  STAX Rp
  MOV R, M
  MOV M, R

## Slide 7
2. Arithmetic Instructions
The frequently used arithmetic operations are: Add, Subtract, Increment (add 1), Decrement (subtract 1)
ADD R
ADI 8-bit
ADD M
SUB R
SUI 8-bit
SUM M
INR R
INR M
DCR R
DCR M
INX Rp
DCX Rp

## Slide 8
3. Logical and Bit Manipulation Instructions
These instructions include the following operations: AND, OR, X-OR, Compare, Rotate bits
ANA R
ANI 8-bit
ANA M
ORA R
ORI 8-bit
ORA M
XRA R
XRI 8-bit
XRA M
CMP R
CPI 8-bit

## Slide 9
4. Branching Instructions
The following instructions change the program sequence.
JMP 16-bit
JZ 16-bit
JNZ 16-bit
JC 16-bit
JNC 16-bit
CALL 16-bit
RET

## Slide 10
5. Miscellaneous Instructions
There are a number of instructions related with data transfer among the register, the stack operation instructions and interrupt operations of 8085 MP which are kept in this group. They are:
PUSH, POP
EI, DI
6. Machine Control Instructions
These instructions affect the operation of the processor.
HLT, NOP